## Slide 1: Sanitary Survey and Identification of Well Pollution and Analysis of Water Quality Using Kits
Prof M.G.Cyriac

## Slide 2: Format for sanitary survey
Type of facility open well or borewell etc
1. General information about the location
Village ...............................................................................
2. Address ................................................................................................
3. Date of visit ......................................
5.sample identification mark
6 Specific diagnostic information for assessment Risk

## Slide 3
Sl No | Specification | Yes / No | Remarks
1 | Is there a latrine within 7.5 m of the well? |  | 
2 | Is the nearest latrine on higher ground than the well? |  | 
3 | Is there any other source of pollution (e.g. animal excreta, rubbish) within 10m of the well? |  | 
4 | Is the drainage poor, causing stagnant water within 2m of the well |  | 
5 | Is the wall (parapet) around the well inadequate, allowing surface water to enter the well |  | 

## Slide 4
6 | Whether the wall of the well inadequately sealed at any point for 3m below ground? |  | 
7 | Whether rope and bucket system is used |  | 
8 | Any attached bathrooms to the well |  | 
9 | Whether the well is not covered |  | 
10 | Whether the foot valve is fixed to the bottom of the well |  | 
11 | Whether sufficient platform of 1 m width is not provided |  | 

## Slide 5
Total score of risks ..................... /11
Contamination risk score: 9–11 =very high; 6–8 =high; 3–5 intermediate; 0–2 low
The following important points of risk were noted: ................................. (list nos 1–11)
and the authority advised on remedial action.
Signature of the Sanitarian

## Slide 6: Attachment to sanitary survey
Sl no | Problem | Reason | Remarks
1 | Turbid | Improper maintenance of well or geogenic problems or other problems | 
2 | Smell | Do | 
3 | Black colour | presence of organic matter or other problems | Identify the pollution source and remove
4 | Sour taste | Low pH | Site specific conditions
5 | Alkaline taste | High pH | Depending on type of source –borewells

## Slide 7
6 | 1)Change in colour when exposed to atmosphere 2)Excess requirement of milk to prepare tea of required flavor 3)Staining in vessels and cloths and bathroom floor 4)Deposition of mud after the water is boiled | Presence of iron | Site specific conditions – more in bore wells

## Slide 8
7 | 1) White deposit on boiling 2) More consumption of Soap | Hardness | 
8 | Salty taste | Chloride presence | Sea water intrusion or geogenic reasons

## Slide 9: Analysis using water analysis kits
1) pH value
2)Iron
3)Fluoride
4)Chloride
5)Nitrate
6)Coliform

## Slide 10: Prominent water quality problems in Kerala
Excess Bacterial presence | Excess conductivity/TDS
Excess iron | Organic pollution measured as BOD/COD
Deviation pH | Excess hardness
Excess turbidity | Excess Nitrate
Excess fluoride | Growth of Algae
Excess Chloride | Carbonate deposition
Presence of Pesticides | 

## Slide 11: 1)PRESENCE OF COLIFORM BACTERIA
Coliform is a group of bacteria present in human excreta
It comprises of 10 % of all the bacteria in human excreta
In water analysis it is used as an indicator of presence of human excreta in water supply
Coliform is present in more than 80 % of our water sources

## Slide 12: COLIFORMS

## Slide 13: REASON FOR SELECTING COLIFORM AS AN INDICATOR
Its presence in human excreta is significant
Out of all the bacteria in human excreta it is the long lived
Its analysis is simple

## Slide 14: LIMITATION OF COLIFORM AS AN INDICATOR
In addition to human being it is present in the excreta of all the hot blooded animals
A strict indicator should not reproduce after discharging in to the surface of earth but in favorable conditions coliform reproduces
Treatmentfor coliform is effective disinfection

## Slide 15: DEVIATION IN PHVALUE
About 60 % of well water samples are having low pH
High pH occurs in limited places
Low pH imparts sour taste and corrosive
nature
Carbon dioxide dissolution from the surface of the earth and subsequent chemical reaction
is the cause for variation in pH value

## Slide 16: CHEMICAL CHANGE WHILE WATER IS PERCOLATED THROUGH THE EARTH

## Slide 17: WATER QUALITY VARIATION WHEN WATER IS PERCOLATED THROUGH THE EARTH
In a shallow well pH will be less but in a deep well or borewell pH will be high
In a deep well hardness, calcium, magnesium ,alkalinity will be more compare to shallow well
Dissolved minerals will also be more in deep water sources

## Slide 18: TREATMENT FOR PH VARIATION
Low pHcan be increased by adding any suitable alkaline substances
Commonly used are lime , soda ash etc
High pHcan be reduced by adding acidic substances

## Slide 19: PRESENCE OF EXCESS IRON
Iron constitutes 6% of the earth crust
3% in soluble Fe2+ form and 3% in insoluble Fe 3+ form
While rain water is percolated through the earth Fe2+ dissolves in the water

## Slide 20: BAD EFFECTS OF IRON
Change in colour when exposed to atmosphere ( oxidation of ferrous Iron to ferric Iron)-
Fe 2+ +O2+H2O Fe(OH)3+H+
Excess requirement of milk to prepare tea of required flavor(Iron +Tanin = black colour)
Staining in vessels
Deposition of mud after the water is boiled
(More oxidation on heating)
Oily appearance on the surface of water

## Slide 21: TREATMENT FOR REMOVAL OF IRON FROM DRINKING WATER
Increase the pH of water by adding suitable alkaline materials ( lime , Soda ash, bleaching powder )
Aerate the water for oxidation to take place
Allow for settling and thereafter for filtering
Disinfect to make it potable

## Slide 22: REMOVAL OF IRON IN OPEN WELLS

## Slide 23
Excess Turbidity

## Slide 24: IRON REMOVAL USING GREEN SAND,IRON SPECIFIC RESIN,BIRM MEDIA

## Slide 26: EXCESS TURBIDITY
It occurs in certain well and in certain water sources
Treatment is plain sedimentation /coagulationsedimentation/ Filtration

## Slide 27: EXCESS FLOURIDE
Flouride dissolves from the crust of the earth
Flouride presence will be more in water sample with less calcium
Ca +F CaF2
In kerala Alappuzha and Palakkad is mainly affected
Domestic kit using activated Alumina is suitale for removal of Flouride

## Slide 28: HEALTH EFFECTS OF FLOURIDE
Excess consumption of flouride results in to Flourosis
Flourosis are three types
Dental Flourosis
Skeletal Flourosis
Non Skeletal Flourosis

## Slide 29: MOTTLING

## Slide 30: CHARACTERISTIC MOTTLING TO TEETH WITH PIGMENTATION

## Slide 31: “Ramaswamy” is the symbol of our dreadful fate, our horrendous sufferings.

## Slide 32: RESTRICTION OF SPINE MOVEMENTS IS AN EARLY FEATURE OF SKELETAL FLUOROSIS

## Slide 34: PRESENCE OF CHLORIDE IN DRINKING WATER
Sea water intrusion in coastal area
In certain open wells in Palakkad district
Ghyben – Hertzberg equation for intrusion of sea water
Commonly used method for treatment for removal of Chloride is Reverse osmosis (RO)
Some (RO) units are being used in coastal area of Kerala

## Slide 35: PRINCIPLE OF REVERSE OSMOSIS

## Slide 37: 2500M3/HOUR UNIT IN JUBAIL , SAUDI ARABIA

## Slide 38: POLLUTION OF WATER SOURCES DUE TO ORGANIC MATTER
Intrusion of waste in to water sources causes pollution
Black colour and death of fish / uneasiness for the fish is manifested
Always remove such waste sources from near the water sources

## Slide 39: HARDNESS
Hardness is caused by multivalent metallic cations
Deep water sources are generally hard
Calcium and Magnesium are generally causes hardness
If topsoil is Thick hardness will be more
Softeners are which remove calcium and magnesium are commonly used for its removal

## Slide 40: CHEMICAL CHANGE WHILE WATER IS PERCOLATED THROUGH THE EARTH

## Slide 41: GROWTH OF ALGAE
In wells water is good in the morning but as sunlight falls color change occurs
Water sources gets polluted
Algae is water plant which requires sunlight for its growth
Treatment for algae growth is prevention of sunlight, chlorine or copper sulphate

## Slide 42: CARBONATE DEPOSITION
As water percolates through the earth CaCo3 dissolves in water Ca(HCO3)2
H2O+CO2 H2CO3
CaCO3+H2CO3 Ca(HC03)2
In deep water sources Ca(HC03)2 will be more and as it is pumped to open areaCO2 starts escaping and CaCO3 starts depositing. Predominant in borewell water

## Slide 44: WATER QUALITY BIS STANDARDS
SLNO | CHARACTERISTICS | UNIT | ACCEPTABLE | CAUSE FOR REJECTION | ACTUAL CONTENTS
1 | Turbidity | NTU | 5 | 10 | 
2 | PH |  | 6.5 to 8.5 | <6.5 & > 8.5 | 
3 | Electrical Conductivity | Micro mhos/cm |  |  | 
4 | Temperature (0C) | mg/litre |  |  | 
5 | Acidity | mg/litre |  |  | 
6 | Alkalinity (Total) | mg/litre | 200 | 600 | 
7 | Total hardness (as Ca CO3) | mg/litre | 300 | 600 | 
8 | Calcium(as Ca) | mg/litre | 75 | 200 | 

## Slide 45
9 | Magnesium (as Mg) | mg/litre | 30 | 150 | 
10 | Chloride (as Cl) | mg/litre | 250 | 1000 | 
11 | Fluoride (as F) | mg/litre | 1.0 | 1.5 | 
12 | Iron(as Fe) | mg/litre | 0.3 | 1.0 | 
13 | Nitrate (as NO3) | mg/litre | 45 | 100 | 
14 | Bacteriological Analysis | No. of Coliforms/ 100 ml |  |  | 
15 | Chemical Oxygen Demand (COD) | mg/litre |  |  | 

## Slide 46: BACTERIOLOGICAL QUALITY (BIS STANDARDS)
Water in distribution system
a. Throughout any year 95% of samples should not contain any coli form organism in 100 ml.
b. No sample should contain E.Coli in 100 ml.
c. No sample should contain more than 10 coliform organisms per 100 ml.
d. Coliform organisms should not be detectable in 100 ml of any two consecutive samples.