## Slide 1: State specific Water quality issues – Remedial measures
M.G.Cyriac

## Slide 2: Water Quality Issues in Kerala State
1)Presence of coliform Bacteria
2)Variation in pH value a)Low pH and high pH
3)Excess Iron
4) Excess Turbidity
5)Excess Flouride
6) Salinity

## Slide 3
Pollution due to organic matter
Excess hardness
Growth of Algae
Deposition of carbonate

## Slide 4: Water Pollution
Point and non point sources of Pollution
Point sources-discharge from an industry, pollution from septic tank of a house etc
Non point sources of pollution,- Pollution of Flouride in Palakkad ,water logged area pollution in Alappuzha

## Slide 5: Classification of the state based on water pollution potential
Water logged area
Coastal area
Thickly Populated Urban area ( towns , cities etc)
Thickly Populated Rural Area
Industrial area
Geographically specific area
Less populated rural area

## Slide 6: Water logged area
Typically most part of Alappuzha district and small parts in other districts
Possibility for pollution is higher
Surface contaminants are having direct access to water bodies
Disposal of human excreta and other wastes are problem
Water contains high organic matter, excessive bacterial presence , turbidity, color, odour and such contaminants
Rain water harvesting is relevant to provide safe water but artificial recharge is not appropriate

## Slide 7: Solutions
Construction of pucca septic tank with inlet and outlet above maximum water level
Reducing the wastes and its effective disposal
Biodegradable solid wastes to be converted as manure using vermi composting
Effective water supply system
Effective treatment even at the household level for to make water potable

## Slide 8: Water Quality Issues in the Coastal Area
Sea water intrusion- Excessive withdrawal of fresh water results in to intrusion of sea water manifested as presence of excess Chloride ,Hardness etc
Predominant in most part of the coastal reach
Excessive presence of chloride , hardness and other minerals and brackisness in the water

## Slide 9: Ghyben- Herzsberg Equation

## Slide 10: Treatments for Chloride Removal
Reverse osmosis

## Slide 13: 2500M3/Hour plant in Jubail, Saudi Arabia

## Slide 14: Remedial measures
Rain Water harvesting
Limited depth of well to draw only fresh water
Other suitable measures to control of draining of fresh water to sea
Treatment of sea water using reverse osmosis
Predominant in Gulf countries

## Slide 15: Thickly Populated Urban Area
In addition to resident population floating population will be enormous
If effective water supply is not available providing safe water to the people is challenging
Waste problem both liquid and solid will be serious
Generally the traditional water sources will be contaminated

## Slide 16: General water quality issues
Presence of coliform bacteria
Presence of excess Iron in drinking water
Presence of organic matter
Low pH and in rare cases high pH
growth of algae
In most cases the pollution can be considered as non point exceptionally point sources of pollution

## Slide 17: Water quality Variation while rain water is percolating through the earth

## Slide 23: Thickly Populated Rural Area
Combined dependence on water supply and and other water sources like wells , borewells , tube wells , filterpoint etc
More than sixty lakhs of open wells are available in Kerala state
Effective maintenance of water supply and other water sources are relevant
Roof top Rain water harvesting and artificial recharge is relevant to control pollution and for sustainability of source

## Slide 24: General water quality issues
Presence of coliform bactera
Presence of excess Iron in drinking water
Presence of organic matter
Low pH and in rare cases high pH
growth of algae
Pollution due to organic matter
In most cases point sources of pollution

## Slide 25: Industrial Area
Pollution from discharge of industrial pollutants
Situation aggravates if the industrial wastes are not properly treated
The pollution depends on the type of industry and its waste products
Public opposition against such industries are common in our state
Artificial recharge reduces pollution

## Slide 26: Remedial measures
Implementation of pollution control legislation-
Effective treatment of industrial wastes
Role of pollution control board is relevant

## Slide 27: Geographically specific area
Alappuzha and Palakkad district having high content of Flouride
Ground water in certain area in palakkad district contains high content of chloride
Certain area in Thrissur district contains high sulphur content in soil which forms sulphate and thereby increases the acidityand reduces the pH
In addition to that so many irregular behaviors
Rain water harvesting and artificial recharge are advantageous

## Slide 28: Excess Flouride

## Slide 29: Less populated rural area
Generally refers to hilly terrain in the state
Generally the people are agriculturist
Houses are located in more area
Comparatively less polluted and healthy
generally open wells are the water sources
Well maintenance is more important Generally the water sources are deep
Rain water harvesting and artificial recharge improves availability of water ,improvement in agricultural activates
Occurrence of point sources of pollution

## Slide 30: Presence of excess Iron
Iron constitutes 6% of the earth crust
3% in soluble Fe2+ form and 3% in insoluble Fe 3+ form
While rain water is percolated through the earth Fe2+ dissolves in the water

## Slide 31: Bad effects of Iron
Change in colour when exposed to atmosphere ( oxidation of ferrous Iron to ferric Iron)-
Fe 2+ +O2+H2O Fe(OH)3+H+
Excess requirement of milk to prepare tea of required flavor(Iron +Tanin = black colour)
Staining in vessels
Deposition of mud after the water is boiled
(More oxidation on heating)
Oily appearance on the surface of water

## Slide 32: Treatment for removal of Iron from Drinking Water
Increase the pH of water by adding suitable alkaline materials ( lime , Soda ash, bleaching powder )
Aerate the water for oxidation to take place
Allow for settling and thereafter for filtering
Disinfect to make it potable

## Slide 33: Removal of Iron in open wells

## Slide 34
Excess Turbidity

## Slide 35: Iron removal using green sand,Iron specific resin,birm media

## Slide 37: Terrafil technology for Iron removal
New method developed by IMMT Bhuvaneswar
Sand,clay and saw dust is mixed in a definite proportion
Thereafter it is moulded in the form of a circular disk
The disk is heated and the saw dust burns away and pores are formed
An iron removal system is arranged in such a way that
Iron containing water is filtered through the disk and the water gets treated

## Slide 38: Terafil technology for water treatment prepare a filtering disk with the following proportion
Sl no | Materials | Percentage
1 | Pottery clay | 58
2 | Wood saw dust | 21
3 | River sand | 21

## Slide 39
Sand, Saw dust & Clay
Mixed with water
Molding of Green Terafil
Production of TERAIL Media (Disc)

## Slide 40
Green Terafil
Sintering of Terafil
Sintered Terafil
Construction of Terafil

## Slide 41
LID
TOP CONTAINER
BOTTOM
CONTAINER
SUPPORT RING
TERAFIL
TAP
TERAFIL WATER FILTER

## Slide 42
A model RCC Chamber for Terafil water filter
Notes: 42

## Slide 43
Assembled of Terafil water filter at IMMT, Bhubaneswar

## Slide 45
TERAFIL WATER FILTER launched by Hon’ble Dy. Chief Minister of Tamilnadu on 25th August 2010 at Chennai

## Slide 46
TERAFIL WATER FILTER launched by Hon’ble Chief Minister of Orissa on 10th August 2007

## Slide 47
Inspection of IMMT technology by Hon’ble MP Sri Rahul Gandhi & Minister S&T, GOI Sri Kapil Sibal at Amethi, UP

## Slide 48
Thank you
Save drinking water